## Slide 1: Chloride Issue in the Chicago Area Waterway System
Sanjay Sofat, Division Manager, Water Pollution Control, Illinois EPA
Sara Terranova, Assistant Counsel, Division of Legal Counsel, Illinois EPA

## Slide 2: Chicago Area Waterway Rulemaking (R08-9)
R08-9 was filed with the Illinois Pollution Control Board in October 2007

## Slide 3: Chicago Area Waterway Rulemaking (R08-9)
Before this rulemaking, these waterbodies were considered as Secondary Contact:
North Shore Channel – Use A - Stretches from the Wilmette Pumping Station and Control Works south to its confluence with North Branch Chicago River, just south of Foster Avenue.
North Branch Chicago River – Use A – Begins at North Branch Chicago River’s confluence with North Shore Channel and flows south to its confluence with both Chicago River and South Branch Chicago River in downtown Chicago. For CAWS rulemaking we proposed the North Branch Chicago River being divided into two reaches:
  the upper reach starts at the confluence with North Shore Channel and ends at the southern end of the North Avenue Turning Basin; and
  the lower reach starts at the southern end of the North Avenue Turning Basin, includes the North Branch Canal (at Goose Island), and ends its confluence with Chicago River and South Branch Chicago River.
Chicago River - General Use – Begins at the Chicago River Lock and Controlling Works at Lake Michigan and stretches to its confluence with both the North Branch Chicago River and South Branch Chicago River.
South Branch Chicago River – Use A – Begins at its confluence with both Chicago River and North Branch Chicago River, and flows south and then west. It ends at its confluence with Chicago Sanitary and Ship Canal at Ashland Avenue in Chicago.

## Slide 4: Chicago Area Waterway Rulemaking (R08-9)
South Fork tributary to South Branch Chicago River - Secondary Contact and IAL - Begins at the MWRDGC Racine Avenue combined sewer pump station and ends at its confluence with South Branch Chicago River.
Chicago Sanitary and Ship Canal (CSSC) – Use B – Begins at its confluence with South Branch Chicago River, flows southwest and then south and ends at its confluence with Des Plaines River. For the rulemaking, the CSSC is divided into two reaches:
  the upper reach starts at the confluence with South Branch Chicago River and ends at its confluence with Calumet-Sag Channel in Willow Springs – Use A; and
  the lower reach starts at the confluence with Calumet-Sag Channel and ends at the confluence with Des Plaines River near the E J & E railroad crossing.
  CSSC also includes the Lockport Control Structure, which diverts stormwater from CSSC water into Des Plaines River to prevent upstream flooding and to protect the downstream lock and powerhouse. It also includes the Lockport Lock and Powerhouse which is used to transfer watercraft upstream and downstream and to generate hydroelectric power.

## Slide 5: Chicago Area Waterway Rulemaking (R08-9)
Lower Des Plaines River – For purposes of the rulemaking the Lower Des Plaines River segment begins at its confluence with CSSC, flows south, and ends at the Interstate-55 bridge crossing. Lower Des Plaines River is sub-divided in this proposal into two reaches:
  the Brandon Road Pool (Use B) reach of the Lower Des Plaines River starts at the confluence of the Lower Des Plaines River and CSSC and ends at the Brandon Road Lock and Dam in Rockdale; and
  Upper Dresden Island Pool (Upper Dresden Island Pool Aquatic Life Use)starts at the Brandon Road Lock and Dam and ends at the Interstate-55 bridge.
Calumet River – Use A - Calumet River begins at Lake Michigan and ends at its confluence with both Little Calumet River and Grand Calumet River. For the rulemaking, Calumet River is subdivided into two reaches:
  the north reach begins at Lake Michigan and ends at the Torrence Avenue crossing in Chicago; and
  the south reach begins at the Torrence Avenue crossing and ends the confluence with both Little Calumet River and Grand Calumet River.
  Calumet River includes the O’Brien Lock and Controlling Works.

## Slide 6: Chicago Area Waterway Rulemaking (R08-9)
Lake Calumet – Use A - Lake Calumet includes the contiguous waters west of Calumet River and north of an imaginary extension of 126th Street that crosses the lake
Lake Calumet Connecting Channel - Use A - The term Lake Calumet Connecting Channel is being used to describe the waters beginning at the southern end of Lake Calumet and ending at the confluence with Calumet River.
Grand Calumet River - Use A - The UAA Grand Calumet River segment begins at the Illinois-Indiana state line in Burnham, flows west, and ends at its confluence with both Calumet River and Little Calumet River. The Grand Calumet River’s flow is reverse of its pre-altered direction.
Little Calumet River - Use A - The UAA part of Little Calumet River begins at its confluence with both Calumet River and Grand Calumet River at the border of Burnham and Chicago, flows west, and the segment ends at its confluence with Calumet-Sag Channel.
Calumet-Sag Channel - Use A - Calumet-Sag Channel is a human-made channel that begins at its confluence with Little Calumet River, flows west-northwest, and ends at its confluence with CSSC.

## Slide 7: Chicago Area Waterway Rulemaking (R08-9)
Three segments of General Use were added:
Chicago River;
Calumet River (from Lake Michigan to the O’Brien Lock and Dam); and
North Shore Channel (from Lake Michigan to the O’Brien WRF).
These segments were originally Secondary Contact and Indigenous Aquatic Life Use (IAL) use waters.

## Slide 9: Chicago Area Waterway Rulemaking (R08-9)
Four sub-dockets were established in March 2010.
  Sub-docket A: Completed. Addressed issues related to Recreational Use designations.
  Sub-docket B: Completed. Addressed issues related to disinfection and whether or not disinfection may or may not be necessary to meet those designations.
  Sub-docket C: Completed, but currently under review by USEPA. Addressed proposed Aquatic Life Uses.
  Sub-docket D: First Notice was published on October 1. 2014. Addresses water quality standards and the criteria which are necessary to meet the Aquatic Life Use designations. First notice comments were submitted in November, 2014.

## Slide 10: Chloride Standard being proposed by the Board in its Frist Notice Opinion and Order
The Board proposed a year round single value of 500 mg/L chloride water quality standard for the Upper Dresden Island Pool, Aquatic Life Use A waters and Aquatic Life Use B waters.
Also, a site specific rule for the Chicago Sanitary and Ship Canal
  December 1 - April 30
    Chronic water quality standard of 620 mg/L
    Acute water quality standard of 990 mg/L

## Slide 11: Other proposals before the Board based on First Notice Comments to the Board
CITGO - Site Specific Rule for the Chicago Sanitary and Ship Canal (proposal Board proposed in its First Notice)
  December 1 - April 30
    Chronic water quality standard of 620 mg/L
    Acute water quality standard of 990 mg/L
MWRD - The Site Specific Rule proposed by CITGO and the Board in its First Notice Opinion and Order should apply to the remaining CAWS reaches and not just the CSSC.
Illinois EPA – Proposed:
  A 500 mg/L standard for the non-winter months (May 1-November 30);
  A winter concept that would utilize best management practices for point sources and non-point sources in winter months;
  A water-body specific variance should one be needed and the need for time to address high chloride concentrations in these waters; and
  Another sub-docket be opened in the rulemaking or that the Board delay a decision with respect to a chloride water quality standard.

## Slide 12: Reports/Data on Chloride Concentrations in Illinois Streams
USGS’s article - Urban Stream Contamination Increasing Rapidly Due to Road Salt
  WI.Water.USGS.gov
The Sources, Distribution, and Trends of Chlorides in the Waters of the Illinois
  Kelly Report
MWRDGC’s Data Network

## Slide 13: Urban Stream Contamination Increasing Rapidly Due to Road Salt
The scientists analyzed water quality data from 30 monitoring sites on 19 streams near cities in WI, IL, CO, MI, OH, PA, MA, TX, and the District of Columbia.
Chloride levels increased substantially in 84% of urban streams analyzed (USGS study from 1960 -2011).
Levels are highest during the winter, but increased during all seasons over time at the northern sites, including Chicago, Illinois.
  In 16 of the streams, winter chloride concentrations increased over the study period.
  In 13 of the streams, chloride concentrations increased over the study period during non-deicing periods such as summer
  Chloride levels increased more rapidly than development of urban land near the study sites.

## Slide 14: Kelly et al. Report, 2012
Chloride Concentrations are High in Surface Waters
  Detailed study that characterizes sources, distribution, and trends of chlorides in IL waters
Increased Use of Chloride for Road De-icing
  An estimated annual average of 471,000 metric tons of road salt were used in Illinois for the years 2002 to 2005, mostly in the Chicago region.
  Average annual road salt sales have increased since 2005.
Findings:
  Chloride concentrations are elevated in most water bodies in the Chicago region, primarily due to road salt runoff.
  Two road salt runoff samples collected by Kelly et al.(2010) dripping off road bridges in Pekin and Willow Springs, IL, had very high concentrations of chloride: 1572 and 8930 mg/L.

## Slide 15: Continued

## Slide 16: MWRDGC
History of Monitoring Program
  Collecting data since 1970
  Currently have at least 28 stations in CAWS watershed that have been collecting data for 10 or more years
Methodology of looking at the District’s data
  Reviewed data from 2001 – 2012
    Chloride concentrations above 500 mg/L, results expressed in percentages
    December – March

## Slide 17: Chloride percentages above 500 mg/L Jan. 2001 through Dec. 2012 (Dec. – March)
North Shore Channel – 8%
North Br. Chicago River – 13%
Chicago River – 2%
South Br. Chicago River – 4.4%
S. Fk. S. Br. Chicago River – 4%
CSSC - 6%
Des Plaines River – 6% (2001 data only)
Calumet River – 0 above 500 mg/L
Lake Calumet – no data
Lake Calumet Connecting Channel – no data
Grand Calumet – 0 above 500 mg/L
Little Calumet River – 2.3%
Cal-Sag - 2.6%

## Slide 18: Possible Scenarios
PCB
CITGO
MWRDGC
IEPA

## Slide 19: Implications on Point and Non-Point Sources
Final water quality standard for the CAWS is still uncertain.
The adoption of a chloride water quality standard (500 mg/L) for CAWS water bodies will result in listing many of these water bodies as impaired for 303d/305b purpose.
  Impaired status
  TMDL
The impaired status of CAWS water bodies will significantly affect point and non-point sources’ ability to do future projects that would add additional chloride loadings to these water bodies.

## Slide 20: Implications
NPDES
MS4
401

## Slide 21: NPDES
New if chloride
Renewed if chloride
Expanded if chloride
Impaired
TMDL
Impaired
TMDL
Impaired
TMDL

## Slide 22: MS4
New General Permit
  Id segment if segment is listed as impaired
  Shall not cause or contribute to violation of any applicable WQS
  If TMDL approved (page 4), then
    Must meet allocations
    Modify storm water management program so that TMDL allocations are met

## Slide 23: Continued
Pollution Prevention/Good Housekeeping for Municipal Operations
Monitoring
  Shall include at a minimum, quarterly monitoring of receiving waters upstream and downstream of MS4 discharges
    Chloride monitoring requirement

## Slide 24: 401
New if chloride
Renewed if chloride
Modified if chloride
Impaired
TMDL
Impaired
TMDL
Impaired
TMDL

## Slide 25: Possible Solutions
Technology Controls
  Limited
  Technically infeasible
  Economically unreasonable
Regulatory Relief
  Adjusted Standard
  Site Specific Standard
  Variance

## Slide 26: Regulatory Relief

## Slide 27: Regulatory Relief
Adjusted Standard
  Provides relief from rules of general applicability.
  Satisfy the “level of justification” specified in the regulation, if any.
  If none, must demonstrate:
    Factors relating to that petitioner are substantially and significantly different from the factors relied upon by the Board in adopting the general regulation applicable to that petitioner;
    The existence of those factors justifies an adjusted standard;
    Relief will not result in environmental or health effects substantially and significantly more adverse than the effects considered by the Board in adopting the rule of general applicability; and
    The adjusted standard is consistent with any applicable federal law.

## Slide 28: Regulatory Relief
Site Specific Rulemaking
  Provides relief from rule of general applicability, but can also be promulgated independently.
  Must specify:
    Reasons why the general rule is not technically feasible or economically reasonable;
    Relevant information regarding other similar sites’ ability to comply with the general rule; and
    Where relevant, information pertaining to existing physical conditions, the character of the area involved, including the character of surrounding land uses, zoning classifications, and the nature of the existing air quality.
  Must demonstrate that the proposal is consistent with federal law.

## Slide 29: Variance
Must comply with two set of requirements
  State requirements
    415 ILCS 5/35(a)
    35 Ill Adm. Code 104.200, et seq.
  Federal requirements
    Proposed Rule Water Quality Standards Regulatory Clarifications, 40 CFR 131 (FR Vol. 78, No. 171/ Wednesday, September 4, 2013)

## Slide 30: Variance – State Regulations
Temporary exemption from any specified rule, regulation, requirement, or order of the Board
Not to exceed five years
Petitioner must provide adequate proof that compliance would impose an arbitrary and unreasonable hardship

## Slide 31: Petition Content Requirements
Data describing the nature and extent of the failure to meet the regulation
Facts demonstrating compliance with regulation cannot be achieved by any compliance date
Efforts that would be necessary to achieve immediate compliance with the regulation
All possible compliance alternatives, with corresponding costs for each alternative
Reasons that immediate compliance would impose an arbitrary or unreasonable hardship
Detailed description of compliance plan
Description of environmental impact
Consistency with Federal Law

## Slide 32: Agency Investigation and Recommendation
The Agency must investigate and consider the views of persons who might be adversely affected by the grant of the variance and make a recommendation to the Board.
Recommendation must include:
  A description of the efforts made by the Agency to investigate the facts as alleged and to ascertain the views of persons who might be affected, and a summary of the views so ascertained;
  A statement of the degree to which the Agency disagrees with facts as alleged;
  Any other facts the Agency believes relevant;
  Estimate of compliance costs;
  Estimate of the injury that the grant of the variance would impose on the public;
  Analysis of applicable federal laws and regulations and an opinion concerning the consistency of the petition with such federal laws and regulations;
  The status of any permits or pending permit applications – including enforcement actions; and
  A recommended beginning and ending date, and any recommended conditions.

## Slide 33: Variance – Federal Regulations
USEPA considers a variance to be a temporary modification to the designated use and associated water quality criteria.
Variances have been based on analyses that meet the requirements governing removal of a use – 40 CFR 131.10(g).

## Slide 34: Removal of Use - 10g Factors
40 CFR 131.10(g) authorizes the removal of a designated use with a demonstration that it is not feasible to attain the designated use of the water body because of any of the following factors:
  Naturally occurring pollutant concentrations prevent the attainment of the use;
  Natural, ephemeral, intermittent or low flow conditions or water levels prevent the attainment of the use, unless these conditions may be compensated for by the discharge of sufficient volume of effluent discharges without violating state water conservation requirements to enable uses to be met;
  Human caused conditions or sources of pollution prevent the attainment of the use and cannot be remedied or would cause more environmental damage to correct than to leave in place;
  Dams, diversions or other types of hydrologic modifications preclude the attainment of the use, and it is not feasible to restore the water body to its original condition or to operate such modification in a way that would result in the attainment of the use;
  Physical conditions related to the natural features of the water body, such as the lack of a proper substrate, cover, flow, depth, pools, riffles, and the like, unrelated to water quality, preclude attainment of aquatic life protection uses; or
  Controls more stringent than those required by sections 301(b) and 306 of the Act would result in substantial and widespread economic and social impact.

## Slide 35: Potential Components of Demonstration
40 CFR 131.10(g)(3) Human Caused Conditions
  Water quality assessment for all relevant parameters
  Biological assessment
  Appropriate reference condition for comparison
  Land usage/watershed characteristics
  Characterization of human caused condition and its relationship to water quality and/or the use in question
  Identification of currently available remedies and assessment of their potential efficacy and feasibility
  Demonstration of application of technology-based requirements and cost effective and reasonable BMPs or forecast of water quality conditions once implemented
  Assessment of potential damage caused by potential remedies

## Slide 36: Potential Components of Demonstration
  40 CFR 131.10(g)(6) Social and Economic Impacts
  Water quality assessment for all relevant parameters
  Biological assessment
  Identification of currently available control technologies and assessment of their potential efficacy,
  Characterization of the costs of controls and their potential for financing over a period of years,
  Characterization of the ability to pay for the affected entities
  Opportunity costs
  Evaluation of equity and distribution
  Environmental justice
  Identification of the community and the characterization of its financial health

## Slide 37: Variance Types
Discharger specific
Waterbody specific
Illinois EPA recommends a waterbody specific variance.

## Slide 38: Requirements
Requirements for waterbody specific variance:
  The highest attainable interim use and interim numeric criterion; or
  An interim numeric effluent condition that reflects the highest attainable condition for a specific permittee(s) during the term of the variance.

## Slide 39: Renewal
10-year term with option to renew is a possibility, but not automatic
USEPA will consider:
  Whether conditions have changed
  Whether new or additional information that the use and criterion are not attainable in the future
  Whether feasible progress is being made toward the designated use and if additional time is needed
Documentation of the steps taken to meet the requirement of the previous variance
Documentation as to whether and to what extent cost-effective and reasonable BMPs have been implemented to address the pollutant
Measure progress and success (monitoring?)
Effect of BMPs

## Slide 40: Proposed Variance Concept
UAA Chloride Variance

## Slide 41: Watershed
What is the watershed?
  UAA

## Slide 42: Applicability to Non-Winter Months
May 1 – November 30
  Basis for non-winter months?
Standard 500 mg/L
  Basis for standard?

## Slide 43: Applicability to Winter Months
December 1 – April 30
  Basis for winter months?
Interim water quality standard:
  No standard
    Focus would be on applying BMPs to point sources and non-point sources to achieve highest attainable stream quality
  Basis for applying BMPs instead of having water quality standard?
    Quantify existing loading
    Quantify existing BMP usage

## Slide 44: BMPs list
Point sources
Non-point sources
Salt Piles (storage handling)
Load limit in NPDES permit in addition to BMPs?

## Slide 45: What we are asking…

## Slide 46: Workgroup
A workgroup responsible for:
  Identifying effective BMPs for point/non-point sources;
  Determining responsibilities for instituting and tracking of BMPs;
  Drafting regulatory language;
  Forming sub-groups if needed;
  Establishing time-frames/deadlines for accomplishing tasks;
  Developing reporting requirements for group and individual sources;
  Establishing accountability requirements (yearly reporting requirements); and
  Establishing and implementing participation requirements.